## Slide 1: The Plant Doctor: Monitoring Plant Health with Machine Learning
Patra Holmes
San Francisco State University
July 30, 2021

## Slide 2: The Plant Doctor Project
Assist agriculture by automating assessment of:
Soil composition
Plant health
Companion planting
Why?
Agriculture a large part of CA economy
  ~ $50B annually
Increasing number of community gardens in urban areas
Can provide a quick scanning tool to
  Save time
  Store data for long-term analysis

## Slide 3: Hand-held OAK-D AI Device
Central 12K RGB color camera
Two monochromatic stereo cameras
  Distance of objects
Built-in AI capabilities with a Myriad X chip
  Object detection
  Classification
  Segmentation
  Tracking
Capable of running multiple Convolutional Neural Networks (CNNs) simultaneously
Affordable - $200
OAK-D device
Inference during live stream
Stereo
cameras
RGB camera

## Slide 4: Components of the Project
Environmental Science
  Soil composition analysis using a colorimetric assay
Anneke Moller, Lorena Benitez Rivera, & Daisy Estrada Reynoso
Phosphorus soil test kit

## Slide 5: Components of the Project
Environmental Science
  Soil composition analysis using a colorimetric assay
Enhanced Spectral Imaging
  Monitors light reflected by the plant outside of the visible spectrum
RBG color camera
Infrared camera
Madu Nzerem & Faye Orcales

## Slide 6: Components of the Project
Environmental Science
  Soil composition analysis using a colorimetric assay
Enhanced Spectral Imaging
  Monitors light reflected by the plant outside of the visible spectrum
Companion Planting
  Different crops in proximity can benefit each other
Berenice Chavez & Maxamillian Schneider

## Slide 7: Components of the Project
Environmental Science
  Soil composition analysis using a colorimetric assay
Enhanced Spectral Imaging
  Monitors light reflected by the plant outside of the visible spectrum
Companion Planting
  Promotes beneficial companion planting
Plant Identification
  To be used by neighbor analysis
Patra Holmes, Johana Aleman, & Amisha Dhawan

## Slide 8: 1) Environmental Science
Automated readings of test kits: reliable and archivable
Nitrogen – chlorophyll
Potassium – roots
Phosphorus – ATP
pH – nutrient solubility
pH test kit
Potassium test kit
Concentrations determined by:
Saturation – depth of color (3 nutrients)
    Beer-Lambert Law
Hue – perceived color (pH)

## Slide 9: 1) Environmental Science
Potassium sample with corresponding plot on a standard curve
OAK-D K Sample - Saturation
sample

## Slide 10: 1) Environmental Science
pH sample with corresponding plot on a standard curve
OAK-D pH Sample - Hue
sample

## Slide 11: OK – Green leaves are an indication of chlorophyll BETTER – Normalized Difference Vegetation Index (NDVI)
2) Spectral Imaging
Healthier plant Higher NDVI

## Slide 12: Spectral Imaging: Tracking Chlorophyll Content
NDVI measured over 2 weeks without water
NDVI
0 1 3 5 7 9 10 12 13
Days without water
Day 0
Day 3

## Slide 13: 3) Companion Planting
Companion planting promotes:
Pollination
Crop productivity
Pest control
Less pesticides
Maximizes the potential of urban gardens
https://diygabl.tumblr.com/post/141353640807/companion-planting-guide
Evaluate existing plants and suggest neighboring plants

## Slide 14: 3D Mapping
Simultaneous identification &
depth information obtained by device
3D map with plant labels

## Slide 15: 4) Plant Identification
What is Machine Learning?
Convolutional Neural Network (CNN) model
Pre-trained models already trained on thousands of images
                Can already extract features
Train model on your own data
https://purnasaigudikandula.medium.com/deep-view-on-transfer-learning-with-iamge-classification-pytorch-5cf963939575
GRAPE
STRAWBERRY

## Slide 16: Types of Convolutional Neural Networks
Conventional CNNs
Single-Shot Detector (SSD) CNNs

## Slide 17: Types of Convolutional Neural Networks
Conventional CNNs
Very large and complex
For classification on computers
  Biological image analysis
  Medical image analysis
Normal tadpole embryo Mutant tadpole embryo
Single-Shot Detector (SSD) CNNs
Tadpole data: Google Colab CSUPERB_Transfer_Learning_Demo
Example of biological use:

## Slide 18: Types of Convolutional Neural Networks
Conventional CNNs
Very large and complex
For classification on computers
  Biological image analysis
  Medical image analysis
Myriad computer chip inside OAK-D runs SSD
Normal tadpole embryo Mutant tadpole embryo
Single-Shot Detector (SSD) CNNs
30x smaller
10x faster
For object detection/classification on small devices
MobileNetv2-SSD for our purposes
Dash cam detection with bounding boxes
Tadpole data: Google Colab CSUPERB_Transfer_Learning_Demo
Example of biological use:

## Slide 19: Curating Leaf Dataset for Plant Identification
Training VGG16 and MobileNetv2-SSD model on leaf image dataset :
8 classes: Orange, Peach, Bell Pepper, Strawberry, Grape, Apple, Tomato, Raspberry
VGG-16: 300 images per class (color only)
MobileNetv2-SSD: 940 images per class: color, -25% brightness, rotated/inverted, B&W
  Bounding boxes placed around leaves
https://www.kaggle.com/abdallahalidev/plantvillage-dataset

## Slide 20: Plant Identification with VGG16 CNN
Training and Testing the model:
Trained on the Kaggle dataset
  300 color per class
Tested with images from Kaggle
  15 per class
  Accuracy of 97%
  Only 4 out of 120 misclassified

## Slide 21: Plant Identification with MobileNetv2-SSD CNN
Training and Testing the model:
Trained on the Kaggle dataset
  300 color
  245 -25% brightness
  245 rotated or inverted
  150 B&W
Tested with images from home garden with OAK-D
  Only 6 available to us
Further data curation can increase:
Classification accuracy
  Bell pepper misclassified
Detection ability
  Two peach leaves undetected

## Slide 22: OAK-D in Action
Classification
% confidence in model’s prediction
Accurately performing leaf detection
Fine-tuning model can increase % confidence

## Slide 23: Plant ID for Both Close-up and Full Plant
Current stage
Future goals

## Slide 24: Can Crop Health Be Improved?
Must consider:
Overall health
Soil composition
Pest control
Pollinator population
  The Plant Doctor App:
  Reduce time spent on monitoring crops
  Store data for long-term analysis
    Help increase yield and quality

## Slide 25: Acknowledgements
NIH MARC: T34-GM008574
NSF STC CCC: DBI-1548297
SFSU & SEO
PINC
BIOL/CHEM 667 Optical Engineering Instructors – Nicole Adelstein, Mark Chan, Raymond Esquerra, & Thomas Zimmerman
OpenCV AI Competition 2021 – Provided access to Microsoft Azure, Intel DevCloud’s openVINO, SuperAnnotate, and OAK-D devices
Roboflow – Object detection training tutorial and data storage